## Slide 1: SECUREOTA A SECURE HETEROGENEOUS OTA UPDATE MECHANISM FOR RESOURCE-CONSTRAINED IOT DEVICES
Final year project | Model examination
Department of Cybersecurity Engineering KCG College of Technology, Chennai
Presented by Priyankaa Devi S (9123128034) | Rithik Sharma A (9123128040) | Ritesh V (9123128039)
Supervisor Dr G. G. Gokilam Project coordinator Dr S. Roselin Mary
Notes: Greet the panel. Introduce the team, our supervisor Dr G. G. Gokilam and our project coordinator Dr S. Roselin Mary. One line: SecureOTA lets a mixed fleet of microcontrollers receive firmware over the air and install it only after proving it is genuine, intact and newer.

## Slide 2: Table of contents
01
Abstract
02
Problem definition
03
Objectives
04
Hardware and software
05
Design diagrams
06
Implementation
07
Results and discussion
08
Conclusion
09
Future enhancements
10
Patent / paper
11
References
12
Questions

## Slide 3: Problem and objectives 01

## Slide 4: Abstract
SecureOTA securely distributes and installs firmware over the air on ESP8266, ESP32, STM32F103 and ATmega328P.
GitHub Actions builds, hashes and signs every release; GitHub Releases distributes it, so no paid server is needed.
Each device runs a five-stage check: connectivity and health, manifest validation, chunk-based download, SHA-256 integrity and Ed25519 signature.
Version tracking, safe installation with self-test, automatic rollback and a persistent health score keep devices running.
Boards too small for Ed25519 hand only the signature check to a nearby gateway.
360 / 360
verification runs ended in the correct state on four boards
950 / 950
attack attempts on the device channel blocked
1.85 KB
peak RAM for full verification; 747 B with the gateway
40 / 40
releases built, signed and published with no manual step
Notes: Read the abstract as the story of the project: the problem, the four building blocks (GitHub Actions, GitHub Releases, five-stage verification, health score), the gateway for the smallest board, then the four results on the right.

## Slide 5: Problem definition
Untrusted firmware delivery
Firmware sent over the air can be altered, swapped for an older version or forged. A device must prove origin and integrity before it installs anything.
Mixed, constrained hardware
One fleet spans the 8-bit ATmega328P with 2 KB of RAM up to the dual-core ESP32. Heavy cryptography and large buffers do not fit the smallest boards.
Manual release and recovery
Hand-built releases lose track of versions, and a failed update on a remote device has no automatic way back and no health record.
Proposed solution
SecureOTA: GitHub Actions builds and signs, GitHub Releases distributes, and every device runs a five-stage verification before a safe, rollback-protected install. A health score tracks each device, and a gateway verifies signatures for boards too small to do it themselves.
Notes: Three challenges. 1: any firmware that arrives over the air must prove where it came from and that it is unchanged. 2: one fleet mixes 8-bit boards with 2 KB of RAM and 32-bit boards, so the security must be light enough for the smallest. 3: building, signing, tracking and recovering firmware by hand does not scale and a bad update can disable a remote device. The box at the bottom is our answer in one sentence.

## Slide 6: Objectives
01
Automated build and signing
GitHub Actions compiles, hashes and Ed25519-signs every release.
02
Five-stage verification
Connectivity, manifest, chunked download, SHA-256, signature.
03
Safe install and rollback
Self-test after boot; automatic return to the last good version.
04
Protected device channel
AES-256-CBC, HMAC-SHA256 and a replay counter on telemetry.
05
Fleet visibility
Version, health score and state of each device on a dashboard.
Measurable objectives
92%
compatibility with existing Arduino sketches
< 3 s
real-time device monitoring latency
96%
integrity validation for transmitted packets
All
firmware releases support version rollback
3 OS
cross-platform execution on Windows, Linux and macOS
Notes: Left: what we set out to build. Right: the five measurable targets; the results section shows each one was met.

## Slide 7: Hardware and software specification
ESP32
Xtensa LX6 dual-core, 240 MHz
520 KB SRAM, 4 MB flash; full five stages
ESP8266
Xtensa L106, 80 MHz
about 80 KB user RAM; full five stages
ATmega328P
8-bit AVR, 16 MHz
2 KB SRAM, 32 KB flash; signature at gateway
STM32F103
Cortex-M3, 72 MHz
20 KB SRAM, 64 to 128 KB flash; full five stages
Layer | Software
Firmware | C++ on Arduino / PlatformIO, mbedTLS, Ed25519 library
Release | GitHub Actions, GitHub Releases REST API
Gateway | Python 3.11, FastAPI, Uvicorn, cryptography
Console | Next.js 16, React 19, TypeScript, Tailwind CSS
Flashing | esptool, esptool-js (Web Serial), USB agent
Deployment | Docker Compose, Cloudflare Tunnel, Raspberry Pi
Notes: Stress the range: from 520 KB of RAM on the ESP32 down to 2 KB on the ATmega328P. All four boards were tested.

## Slide 8: System design 02

## Slide 9: 6.1 Overall design
Release pipeline
Version tag starts build
SHA-256 digest, manifest
Ed25519 signature
GitHub Releases
OTA gateway (FastAPI)
Releases, signed manifests
Deployments per device
Device registry, tokens
Heartbeats, health score
Device fleet
ESP32 node
ESP8266 node
ATmega328P node
STM32F103 node
Arrows: publish, firmware and manifest, heartbeats
Operator console
Live fleet, releases, deployments
REST + live stream
USB flash and provisioning (first install)
All updates after the first install travel over the air.
Notes: Left to right: the release pipeline builds, hashes, signs and publishes; the gateway serves signed manifests and firmware and receives heartbeats; devices verify before installing. The console sits on the gateway and is also used once per board for the first USB flash.

## Slide 10: 6.2 Detailed design
Developer
pushes version tag v2.1.0
GitHub Actions
compile, SHA-256, manifest, Ed25519 sign
GitHub Releases
binary + signed manifest.json
Device agent
five-stage verification
Safe install
self-test, confirm or roll back
manifest.json: checked before the firmware is downloaded
Field | Example | Purpose
version | 2.1.0 | Compared with the version stored on the device
sha256 | 64 hex characters | Integrity check of the downloaded binary
size | 524288 | Rejects truncated or oversized files early
target_boards | esp32, esp8266 | Only compatible boards accept it
signature | Base64, 64 bytes | Ed25519 over version, sha256 and size
rollback_safe | true | Previous version may be restored
Trust anchors
Ed25519 private key stored as a GitHub Actions secret: usable by the workflow, never readable
32-byte public key compiled into every device firmware
Gateway key fingerprint shown in the console, so an operator can confirm the right key
Notes: Walk the top row left to right: a tag starts the build, the workflow hashes and signs, the release holds binary and manifest, the device verifies in five stages and only then installs. Below: what the manifest carries and where the keys live.

## Slide 11: 6.3 Algorithm design
S1
Connectivity and health
H <= 40: quarantine; unreachable: -1
S2
Manifest validation
missing field -10; version mismatch -15
S3
Chunk-based download
size mismatch -15
S4
SHA-256 integrity
digest mismatch -20
S5
Ed25519 signature
invalid signature -30
Any stage fails: discard the image, keep running the current firmware, lower the health score H
All five pass (D = 1)
image already in the inactive partition
Reboot and self-test
network, gateway, hardware
Pass: confirm
save version, H + 10
Fail: roll back
previous partition, H - 25
Install decision D = s1 × s2 × s3 × s4 × s5, si ∈ {0, 1}
Version rule install only if v_new > v_current
Health update H(k+1) = min(100, max(0, H(k) + Δ(event)))
Quarantine H ≤ 40: stop updating until an admin reset
Peak RAM 1,847 bytes on ESP32, ESP8266 and STM32F103; 747 bytes on ATmega328P with S5 at the gateway.
Notes: Each stage is cheaper than the next, so bad updates are dropped early. Any failure discards the image, keeps the running firmware and lowers the health score by an amount that matches how suspicious the failure is. Only when all five pass (D = 1) is the image installed.

## Slide 12: Implementation 03

## Slide 13: Implementation: modules
M1 Device update agent
Five stages, chunked download
M2 Gateway-assisted check
Ed25519 for the ATmega328P
M3 Signing and release
GitHub Actions to Releases
M4 Version, install, rollback
Dual partition, self-test
M5 Health score and quarantine
Persistent score in NVS
M6 Edge gateway service
FastAPI, signed manifests
M7 OTA IDE control plane
Next.js console and roles
M8 Secure device channel
Five layers of protection
M9 Deployment
Docker, edge, tunnel
Notes: Nine modules. M1 to M5 run on or for the device, M6 and M7 are the server side, M8 protects the device channel, M9 is how it is deployed. The next nine slides take each one in turn.

## Slide 14: M1 Device-side update agent
C++ on Arduino and PlatformIO; the same agent runs on all four boards and is called on every scheduled update cycle.
How it works
1 Reads the health score from NVS. At 40 or below the device is quarantined and skips the cycle; otherwise it asks the release API for the newest version (S1).
2 Downloads only the small manifest.json first and checks every required field, the version against the release tag, the file size against the free OTA partition, and the board type (S2).
3 Streams the binary in fixed chunks: each chunk is written straight to the inactive OTA partition and fed into a running SHA-256 (S3). The same 512-byte buffer is reused, so memory does not grow with image size.
4 Compares the final digest with the manifest; any mismatch erases the partition (S4).
5 Verifies the Ed25519 signature over version, sha256 and size with the public key compiled into the firmware (S5).
6 Only then switches the boot partition and reboots into a self-test (see M4).
Design decision manifest first, binary second, and hashing while downloading: a file of any size is verified with one chunk-sized buffer.
Chunk size per board
Chunk | Buffer | Loops for 512 KB | Used on
256 B | 256 B | 2,048 | ATmega328P
512 B | 512 B | 1,024 | ESP8266, STM32
1,024 B | 1 KB | 512 | ESP32
Working memory per stage (bytes)
Stage | ESP / STM32 | ATmega328P
S1 Connectivity and health | 48 | 48
S2 Manifest validation | 124 | 124
S3 + S4 Download and SHA-256 | 768 | 512
S5 Ed25519 | 1,520 | gateway
Peak | 1,847 | 747
Notes: Explain the order: the manifest is tiny, so checking it first avoids wasting bandwidth and battery on a download that would be rejected, and it blocks an attacker who serves a huge file to exhaust the device. The chunk loop is the longest-running part: read a chunk, write it at the current offset of the inactive partition, update SHA-256, reuse the buffer. Chunk size is a per-board setting: 256 bytes on the ATmega328P, 512 on ESP8266 and STM32F103 (default), 1 KB on the ESP32. Measured peak RAM for the whole check is 1,847 bytes: stage 1 uses 48 bytes, stage 2 124, download and hash 768, Ed25519 1,520.

## Slide 15: M2 Gateway-assisted verification
Used where required: on the ATmega328P, Ed25519 does not fit next to the application in 2 KB of RAM.
How it works
1 The ATmega328P runs S1 to S4 itself: health check, manifest validation, chunked download and the SHA-256 comparison.
2 If S4 passes, it sends the gateway only the 64-byte signature and the signed message: version, sha256 and size joined together.
3 The gateway runs the Ed25519 verification with the same public key the other boards hold.
4 It answers with a single byte: pass or fail.
5 The ATmega installs only on a pass. A fail, or no answer before the timeout, is treated as a rejected update and lowers the health score.
6 The firmware image itself never leaves the device, and the gateway cannot make the device install anything it has not already hashed.
Design decision split the work, not the trust: the device keeps the integrity check and the gateway only confirms the signature, so even an 8-bit board joins a signed update process.
ATmega328P
Gateway
S1 to S4 on device
health, manifest, download, SHA-256
signature + version ‖ sha256 ‖ size
S5 Ed25519 verify
about 1.5 KB RAM
1 byte: PASS / FAIL
PASS: install
FAIL or timeout: reject, lower H
Notes: This is how the project meets the requirement "gateway-assisted verification where required". The ATmega328P has 2 KB of SRAM in total; Ed25519 needs about 1.5 KB of working memory on its own. With S5 moved to the gateway the ATmega peaked at 747 bytes, under our 800-byte design limit. The cost is that a gateway must be present and reachable. Stress that the message the gateway checks is exactly the one the release workflow signed, so the gateway cannot be tricked into approving a different binary.

## Slide 16: M3 Signing and release automation
A GitHub Actions workflow in YAML; the only human step is pushing a version tag.
How it works
1 Pushing a semantic version tag (for example v2.1.0) starts the workflow automatically.
2 The firmware is compiled for each target board; the workflow computes the SHA-256 digest and size of every binary.
3 It writes manifest.json and signs version, sha256 and size with the Ed25519 private key, read from the encrypted GitHub Actions secrets.
4 It publishes a GitHub Release with the binary and the signed manifest attached, and records the release in the local version file.
5 At build time a small tracking component is injected into the generated code, so the developer's sketch is not edited. On the ESP32 it runs on the second core.
6 The key pair was generated once with OpenSSL; rotating it means a new secret and new firmware with the new public key.
Design decision GitHub is the build server, the signing service and the download server, so the project needs no paid infrastructure and every release is reproducible.
git tag v2.1.0 pushed
workflow starts
Compile per board
Arduino / PlatformIO
SHA-256 + size
manifest.json written
Ed25519 sign
key from Actions secret
Publish GitHub Release
binary + signed manifest
40 of 40 runs succeeded; ESP32 48.8 s end to end
Notes: Because the workflow is triggered by the tag, a release cannot be published without being built, hashed and signed in the same run; there is no way to upload an unsigned binary by mistake. Measured over 10 runs per board: ATmega328P 13.5 s, STM32F103 16.5 s, ESP8266 27.9 s, ESP32 48.8 s end to end; 40 of 40 runs succeeded. The private key never leaves GitHub: a secret can be used by the workflow but cannot be read back or displayed.

## Slide 17: M4 Version tracking and rollback
Dual OTA partitions: the running firmware is never overwritten until the new one has proven itself.
How it works
1 The current version is stored in NVS and compared as major, minor and patch numbers; only a strictly newer version is accepted, which blocks downgrade attacks (-20 to H).
2 The verified image already sits in the inactive partition; the agent switches the boot partition and reboots into it as "pending".
3 A self-test checks Wi-Fi, the gateway connection and the board's hardware.
4 Pass: the image is confirmed, the new version is written to NVS and the health score rises by 10.
5 Fail: the bootloader returns to the previous partition automatically and the health score drops by 25.
6 Every release stays on GitHub with its source commit, so the console can roll a device back to any earlier version.
Design decision the version number is written only after the self-test passes, so a failed update can never advance the recorded version.
Verified image
in the inactive partition
Switch boot partition
reboot as pending
Self-test
Wi-Fi, gateway, hardware
Pass: confirm
save version, H + 10
Fail: roll back
previous image, H - 25
7 of 7 rollbacks restored, mean 7.31 s
Notes: Write-ahead order matters: if power is lost during the update, the device boots the old partition and its stored version still matches what it runs. Measured: 8 of 8 versions tracked locally and on GitHub; 7 of 7 rollbacks restored with a matching SHA-256; mean rollback time 7.31 s, rising from 6.9 to 7.8 s with image size, so rollback cost depends on size, not on how far back the version is. Each rollback adds its own ROLLBACK entry to the history instead of erasing it.

## Slide 18: M5 Health score and quarantine
Anomaly-scored health (ASH): a persistent 0 to 100 score per device, kept in NVS and reported in every heartbeat.
How it works
1 The score is a running ledger of the device's security history, not a counter that resets each cycle.
2 Every event with security meaning changes the score by an amount that matches how suspicious it is (table).
3 Each change is written to NVS before the agent takes the next step, so cutting the power cannot erase a pattern of suspicious events.
4 At 40 or below the device enters quarantine: it stops accepting updates and reports its state.
5 Only an administrator reset from the console restores the score to 100.
6 The gateway also excludes quarantined devices when it offers new releases.
Design decision write-ahead scoring: the score on the next boot always reflects every event already processed, even after a power cut.
Event | ΔH
Successful update | +10
Poll, no update needed | +1
Server unreachable | -1
Manifest field missing | -10
Version differs from release tag | -15
File size mismatch | -15
SHA-256 mismatch | -20
Older version offered | -20
Self-test failed, rolled back | -25
Ed25519 signature invalid | -30
Admin reset | = 100
Notes: Walk through the table: network problems cost little because they are often innocent; a bad signature costs most because it needs either a forged key or a serious misconfiguration. Three or more failures in one session cost an extra 15, which catches persistent attacks. In testing, one device followed through an attack sequence reached quarantine exactly as the table predicts, and a manual reset restored it to 100 in all 40 runs.

## Slide 19: M6 Edge gateway service
Python FastAPI application served by Uvicorn; owns all server-side state for the fleet.
How it works
1 Split into modules: configuration, request models, cryptography, state, release logic and route handlers.
2 All state lives in one JSON document written atomically on every change, so there is no database to run.
3 On first start it generates an Ed25519 signing key (PKCS8 PEM), loads it on later starts, and shows a SHA-256 fingerprint of the public key.
4 Uploading a release computes the digest and size, builds the manifest and signs it.
5 On every start it re-hashes the cached firmware and re-signs the manifest, so the signature always describes the bytes actually served.
6 A heartbeat returns update_available only for a release that matches the board's architecture, is strictly newer, and goes to a device that is not quarantined.
Design decision filter by architecture before offering an update, so an ESP8266 is never offered an ESP32 image that would verify and then fail to run.
Endpoint | Method | Purpose
/api/heartbeat | POST | Telemetry in; update_available out
/api/releases | POST | Create release, sign manifest
/releases/latest/manifest | GET | Signed manifest for devices
/releases/latest/public-key | GET | Ed25519 public key
/releases/download/{file} | GET | Firmware from the cache
/api/deployments | POST | Roll out to a device set
/api/dashboard | GET | Fleet view for the console
/healthz | GET | Liveness probe
Notes: The gateway is what lets the project run without a paid cloud: it can sit on a laptop, a server or a Raspberry Pi next to the devices. Point at the API table: devices only use the heartbeat, manifest, public key and download endpoints; operators use releases and deployments, which need the API key. Requiring "strictly newer" at the gateway avoids offering a downgrade that the device would reject seconds later.

## Slide 20: M7 OTA IDE control plane
Next.js 16 and TypeScript: one authenticated console for the whole platform.
How it works
1 Sign-in uses scrypt password hashes; session tokens are stored only as SHA-256 digests, so a leaked database does not leak sessions.
2 Three roles: admin, operator and viewer. Flashing, publishing and deploying need operator rights; every write request is recorded in an audit log.
3 Devices page: per-device firmware version, health score and last-seen time, plus first-time setup over USB (Web Serial or the local agent) that writes Wi-Fi, gateway URL and a device token.
4 Releases page: release history, assets and compatibility; a local build can be published with its factory image in one step.
5 Monitoring pages show the five-stage verification status and the health score trend and quarantine state of each device.
6 The local command endpoint is off by default and, when enabled, runs only allowlisted commands.
Design decision the console never holds the firmware signing key; it can publish and deploy, but only the release workflow and gateway can sign.
Page | What it does
Dashboard | Fleet summary, health distribution
Devices | Version, health, last seen, USB setup
Releases | History, assets, publish a build
Manifest | Field-by-field view of the signed manifest
Verification | Five-stage status per device
Health monitor | Score trend, quarantine, reset
Profile | Users, roles, sessions
Notes: This replaces a terminal, curl commands and a serial monitor with one place where the risky actions have confirmation and permissions. Dashboard updates reached the screen in 1.24 s on average and 2.40 s at worst with 10 devices, under the 3-second target. The same console was tested on Windows 11, Ubuntu 22.04 and macOS 14: 6 of 6 functions on each.

## Slide 21: M8 Secure device channel
Telemetry between device and console is protected by five independent layers.
How it works
1 AES-256-CBC encrypts every packet, so an observer on the network sees only ciphertext: no device IDs, versions or health scores.
2 HMAC-SHA256 tags each packet; any change in transit breaks the tag, so integrity and origin are checked together.
3 A device identity registry accepts telemetry only from MAC addresses recorded when the board was provisioned.
4 A strictly increasing packet counter, stored in NVS so it survives reboots, makes any replayed packet arrive with an old number and be dropped.
5 Firmware pushed from the console is signed (ECDSA P-256) and verified on the device, so a forged image is refused even if it is delivered.
6 An attacker needs every key, a registered identity and a fresh counter at the same time; missing any one stops the attack.
Design decision defence in depth: each layer covers a different attacker capability, so defeating one layer does not defeat the channel.
Layer | Stops | Blocked
AES-256-CBC | Packet sniffing | 200 / 200
HMAC-SHA256 | Tampered packet | 200 / 200
MAC registry | Unregistered device | 200 / 200
NVS counter | Replayed packet | 200 / 200
ECDSA P-256 | Forged firmware | 50 / 50
AES / padding | Corrupted key | 50 / 50
SHA-256 | Wrong hash in metadata | 50 / 50
950 of 950 attempts blocked; 97.3% of 6,000 genuine packets validated
Notes: Explain why one layer is not enough: encryption alone stops reading but not tampering; HMAC alone stops tampering but not reading; identity checks stop unknown devices but not a captured packet; the counter stops replay but nothing original. Measured: 950 of 950 hostile attempts were stopped by the layer responsible, and 97.3% of 6,000 genuine packets validated, 94.8% even at -85 dBm.

## Slide 22: M9 Containerised deployment
The gateway and the console ship as containers, so a deployment is reproducible instead of a list of manual steps.
How it works
1 Docker Compose starts the gateway and the console together; settings come from one environment file.
2 The stack refuses to start while the sample administrator password or gateway API key is still in place.
3 Signing keys live in a Docker volume generated on first start, never in the repository.
4 Edge profile: the gateway on a Raspberry Pi Zero 2 W next to the devices. A 1 MB update for 100 boards crosses the internet once (1 MB) instead of 100 times (100 MB).
5 The edge gateway can also isolate a device whose health score has collapsed at the network level.
6 For remote access, a Cloudflare Tunnel publishes the console and gateway over HTTPS without opening inbound ports.
Design decision the same containers run on a laptop, a lab server or a Raspberry Pi; only the deployment profile changes.
Mode | Release source | Suited to
Hosted | GitHub Releases | Small fleets, no server
Self-hosted | Gateway on LAN | Private firmware
Containerised | Gateway + console | Labs, institutions
Edge | Raspberry Pi gateway | Slow or metered links
100 boards × 1 MB update
Edge gateway: 1 MB over the internet. Without it: 100 MB.
Notes: Choose the mode by the site: hosted mode needs no server at all (GitHub Releases only); a self-hosted gateway suits private firmware; containers suit a lab or institution; the edge profile suits slow or metered links. One script brings the stack online and checks each step: containers healthy, tunnel registered, public address answering.

## Slide 23: Implementation: platform
Devices page of the SecureOTA console
Platform security
▪ Per-device tokens, revocable from the console
▪ Roles: admin, operator, viewer
▪ Audit log of every write request
▪ No private keys in the repository
1. Build
Full image, signed OTA package, build info
2. First flash
Browser or USB agent; writes Wi-Fi, gateway, token
3. Publish and deploy
Devices update on their next heartbeat
4. Monitor
Status, health score, events, audit log
Notes: Demo order: build, first flash over USB, publish and deploy, monitor. Mention per-device tokens, roles and the audit log.

## Slide 24: Implementation status by board
Board | Reaches gateway | Stage 5 (Ed25519) | Install and recovery | Verified so far
ESP32 | Wi-Fi | On the board | Dual partition, automatic rollback | Compiles; earlier build ran on hardware
ESP8266 | Wi-Fi | On the board, inside Update.end() | eboot copy; failed version skipped | Compiles for NodeMCU
STM32F103 | UART link host | On the board (Monocypher) | Staged in SPI flash; copy bootloader to do | Compiles; PC end-to-end test
ATmega328P | UART link host | Gateway-assisted, one-bit answer | DualOptiboot copy from SPI flash | Compiles (1.4 KB RAM); PC end-to-end test
Shared code one C library (sota_core) builds the signed statement and checks it on every board; 216 gateway tests, the native library test and 7 end-to-end UART tests pass.
Notes: Be exact about what exists. All four boards have firmware that compiles for the real chip. The ESP32 has run on hardware. The UART agent used by the ATmega328P and STM32F103 was tested end to end on a PC against the real gateway, including a flipped byte, a forged signature, a downgrade and a failed self-test. The STM32F103 copy bootloader is the one missing piece.

## Slide 25: Results and conclusion 04

## Slide 26: Results: test case summary
Test cases by category
Category | Cases | What is tested
Functional | 14 | Compile, discovery, encryption, signing, history, rollback
Security | 7 | Sniffing, MITM injection, forged firmware, replay
Fault tolerance | 5 | Wi-Fi drop and power loss mid-upload
Regression | 5 | USB upload, Serial Monitor, Board and Library Manager
Total | 31 | All documented cases passed
Evaluation volume and results
Evaluation | Volume | Passed | Rate
Arduino sketch compatibility | 60 sketches | 56 | 93.3%
Verification runs (9 x 4 boards x 10) | 360 runs | 360 | 100%
Attack attempts on the channel | 950 | 950 blocked | 100%
Telemetry packet integrity | 6,000 packets | 5,839 | 97.3%
Dashboard state changes | 30 | 30 | 100%
Version rollbacks | 7 | 7 | 100%
Cross-platform functions (6 x 3 OS) | 18 | 18 | 100%
Notes: Left: the 31 planned test cases by category. Right: the volume of each evaluation and how much passed.

## Slide 27: Results: measurable objectives
Measurable objective | Target | Achieved | Status
Arduino sketch compatibility | 92% | 93.3% (56 of 60) | Met
Real-time monitoring latency | Below 3 s | 2.40 s worst, 1.24 s mean | Met
Packet integrity validation | 96% | 97.3% (5,839 of 6,000) | Met
Rollback for all releases | All releases | 8 of 8 tracked, 7 of 7 rolled back | Met
Cross-platform execution | Windows, Linux, macOS | 6 of 6 functions on all three | Met
93.3%
of existing sketches run unchanged
2.40 s
worst-case dashboard update with 10 devices
97.3%
of packets validated; 94.8% even at -85 dBm
Notes: All five targets met. Margins on the percentage targets are modest (1.3 points each), so present them as met, not far exceeded.

## Slide 28: Results: five-stage verification
No. | Scenario | Runs | Passed | Rate | Health effect
1 | Clean update, older to newer version | 40 | 40 | 100% | +10
2 | Mismatched SHA-256 checksum rejected | 40 | 40 | 100% | -20
3 | Invalid Ed25519 signature rejected | 40 | 40 | 100% | -30
4 | Older (downgrade) version rejected | 40 | 40 | 100% | -20
5 | Manifest with a missing field rejected | 40 | 40 | 100% | -10
6 | Health score change correct per failure type | 40 | 40 | 100% | per table
7 | Quarantine after accumulated failures | 40 | 40 | 100% | H ≤ 40
8 | Self-test failure triggers automatic rollback | 40 | 40 | 100% | -25
9 | Manual reset clears quarantine | 40 | 40 | 100% | restored to 100
 | Total (ESP32, ESP8266, STM32F103, ATmega328P) | 360 | 360 | 100% | 
Notes: 9 scenarios, each run 10 times on each of the four boards: 360 runs. A run passes only if the device ends in the correct state: the valid update installed, or the old firmware still running with the correct health penalty. The ATmega328P passed the signature scenario through the gateway.

## Slide 29: Results: memory and signature cost
Chart: Working memory per stage (bytes)
| S1 | S2 | S3 + S4 | S5 | Peak
Working memory (bytes) | 48 | 124 | 768 | 1520 | 1847
2 KB target; ATmega328P peak 747 B with S5 at the gateway
Metric (ESP8266, 80 MHz) | Ed25519 | RSA-2048
Public key size | 32 bytes | 256 bytes
Signature size | 64 bytes | 256 bytes
Working RAM to verify | about 1.5 KB | about 64 KB
Verification time | 23 ms | 3,200 ms
Security level | ≈ RSA-3072 | RSA-2048
Constant-time | Yes | No
RSA-2048 needs more RAM than the ATmega328P and STM32F103 have together.
Notes: Left: working memory of each stage on the 32-bit boards; the peak, 1,847 bytes, is under the 2 KB target. Right: why Ed25519 was chosen for the signature: on the ESP8266 it needs about 43 times less RAM and is about 139 times faster than RSA-2048.

## Slide 30: Results: automated release pipeline
Chart: seconds
| ATmega328P | STM32F103 | ESP8266 | ESP32
Compile | 9.8 | 12.3 | 21.4 | 38.6
Checksum and manifest | 0.4 | 0.4 | 0.5 | 0.6
Signing | 0.2 | 0.2 | 0.2 | 0.2
Publish | 3.1 | 3.6 | 5.8 | 9.4
40 / 40
releases built, hashed, signed and published automatically
48.8 s
ESP32, tag to published release; 13.5 s on the ATmega328P
7 / 7
rollbacks restored with a matching SHA-256, mean 7.31 s
Notes: Mean of 10 runs per board. Compile time dominates and grows with binary size; checksum, manifest and signing together take under a second. All 40 runs completed; the only human action was creating the tag.

## Slide 31: Conclusion
Zero-cost, automatic releases
GitHub Actions and GitHub Releases build, sign and distribute every version; 40 of 40 releases with no manual step.
Fits 2 KB devices
Ed25519 and chunked hashing keep full verification at 1,847 bytes; the ATmega328P joins through the gateway at 747 bytes.
Self-protecting fleet
Five-stage checks, self-test, rollback and the health score kept every device in the correct state in 360 of 360 runs.
SecureOTA delivers authenticated, integrity-checked and recoverable firmware updates across four microcontroller families, with all five measurable objectives met and no paid infrastructure.
Notes: Three results, one per card, then the bottom line. Mention the honest limits if asked: the ATmega328P needs a reachable gateway, and GitHub API rate limits matter for very large fleets; both are manageable for small and medium fleets.

## Slide 32: Future enhancements
01
Delta updates
Send only changed bytes (bsdiff)
02
Lighter signatures
Post-quantum, low-energy schemes
03
Fleet analytics
Health history across devices
04
Key rotation
Rotate signing keys over the air
05
Energy per update
Measure cost on battery nodes
06
Larger fleets
Caching beyond API rate limits
Notes: Delta updates are the most useful next step for slow links. Lightweight post-quantum signatures are the next step for the cryptography once libraries mature.

## Slide 33: Patent / paper publications
Conference paper
SecureOTA: A Secure Heterogeneous OTA Update Mechanism for Resource-Constrained IoT Devices
Priyankaa Devi S, Rithik Sharma A, Ritesh V and the project guide, KCG College of Technology
Item | Detail
Status | Prepared for submission
Submission | Will be submitted to the upcoming IEEE conference
Format | IEEE conference paper, 16 references
Patent
Not yet filed
The patent application is not ready and has not been submitted. Candidate elements: the five-stage verification pipeline with gateway-assisted signature checking, and the health-score quarantine loop.
Notes: Paper: prepared, to be submitted to the upcoming IEEE conference. Patent: not ready, not submitted. Do not claim acceptance or filing.

## Slide 34: References (1 of 2)
[1] Noprianto, N. Funabiki, H. H. S. Kyaw, K. C. Brata, I. N. D. Kotama, "A proposal of secure and automated over-the-air firmware update mechanism for IoT devices using CI/CD," Sensors, vol. 26, no. 5, 1535, 2026.
[2] H. S. Mehdy, M. E. Rusli, H. K. Hoomod, "A secured parallel multi-broker MQTT framework with chaos-enhanced hybrid encryption for repetition-resistant IoT security," Computers, vol. 15, no. 10, 650, 2026.
[3] G. Amirkhanova et al., "A lightweight, end-to-end encrypted data pipeline for IIoT: An AES-GCM implementation for ESP32, MQTT, and Raspberry Pi," Information, vol. 17, no. 1, 33, 2026.
[4] W. Y. Leong, "Quantum-resistant encryption for IoT communication in critical engineering infrastructure," Eng. Proc., vol. 134, no. 1, 76, 2026.
[5] C.-Y. Park, S.-J. Lee, I.-G. Lee, "Secure and lightweight firmware over-the-air update mechanism for Internet of Things," Electronics, vol. 14, no. 8, 1583, 2025.
[6] L. Formanek, M. Kubaščík, O. Karpíš, P. Kolok, "Advanced system for remote updates on ESP32-based devices using over-the-air update technology," Computers, vol. 14, no. 12, 531, 2025.
[7] F. Serepas et al., "Lightweight embedded IoT gateway for smart homes based on an ESP32 microcontroller," Computers, vol. 14, no. 9, 391, 2025.
[8] C.-G. Dumitrache, P. Anghelescu, "Design and implementation of a secure communication architecture for IoT devices," J. Sens. Actuator Netw., vol. 14, no. 4, 64, 2025.
Notes: Do not read these out; point to them if asked about a source.

## Slide 35: References (2 of 2)
[9] V. P. Ojha, S. Chauhan, S. Yarahmadian, D. Carvalho, "Unfolding post-quantum cryptosystems: CRYSTALS-Dilithium, McEliece, BIKE, and HQC," Mathematics, vol. 13, no. 17, 2841, 2025.
[10] Y. Shin, S. Jeon, "MQTree: Secure OTA protocol using MQTT and MerkleTree," Sensors, vol. 24, no. 5, 1447, 2024.
[11] V. Bhargava, N. S. Raghava, "Version control system gateway to optimize firmware over the air (FOTA) update for IoT wireless devices," Wireless Pers. Commun., vol. 134, no. 1, pp. 249-265, 2024.
[12] C. Silva, V. A. Cunha, J. P. Barraca, R. L. Aguiar, "Analysis of the cryptographic algorithms in IoT communications," Inf. Syst. Front., vol. 26, pp. 1243-1260, 2024.
[13] I. Radhakrishnan, S. Jadon, P. B. Honnavalli, "Efficiency and security evaluation of lightweight cryptographic algorithms for resource-constrained IoT devices," Sensors, vol. 24, no. 12, 4008, 2024.
[14] F. C. Andriulo, M. N. Postorino, "Edge computing and cloud computing for Internet of Things: A review," Informatics, vol. 11, no. 4, 71, 2024.
[15] L. Carnevale et al., "Secure and energy efficient filtered over-the-air Internet of Things setup in a wireless mesh network for firmware freshness," Proc. IEEE BigData, Sorrento, Italy, pp. 3904-3913, 2023.
[16] Z. Dewamuni, B. Shanmugam, S. Azam, S. Thennadil, "Bibliometric analysis of IoT lightweight cryptography," Information, vol. 14, no. 12, 635, 2023.

## Slide 36: Thank you
Questions are welcome
priyankaa786sk@gmail.com
a.rithiksharma@gmail.com
v.riteshvijaykumar@gmail.com
Notes: Thank the panel and invite questions.