## Slide 1
FINAL YEAR PROJECT | MODEL EXAMINATION
SecureOTA: A Secure Heterogeneous OTA Update Mechanism for Resource-Constrained IoT Devices
Signed firmware, verified cheapest check first, and a live view of every device, on low-cost microcontrollers.
PRESENTED BY
Priyankaa Devi S
9123128034
Rithik Sharma A
9123128040
Ritesh V
9123128039
SUPERVISOR
[Supervisor name]
PROJECT COORDINATOR
[Project coordinator name]
HOW AN UPDATE TRAVELS
Build and sign
Version tag starts the CI build; SHA-256 digest is signed
Publish and deliver
Signed bundle and manifest reach devices over HTTPS
Verify in five gates
Cheapest checks first; signature check last
Boot, self-test, report
Commit or roll back; health score and beacon update
Notes: Introduce the team and the title. One sentence on what SecureOTA is: a firmware update mechanism that keeps updates and device status from being forged, tampered with or replayed, and that rejects bad updates cheaply on small microcontrollers. Point at the right panel: this is the journey of one update, and the rest of the talk follows it.

## Slide 2: Abstract
What we built and what we measured, in one slide
IoT fleets are hard to secure: devices are out of sight after deployment, and many update paths never check a signature.
SecureOTA is a firmware lifecycle framework for ESP32, ESP8266, STM32F103 and ATmega328P devices.
Firmware is hashed with SHA-256 and signed with Ed25519 in a GitHub Actions workflow. Device status beacons are encrypted with AES-256-CBC and tagged with HMAC-SHA256 and a persistent counter, so they cannot be forged or replayed.
Each update passes five verification gates ordered by cost and rejection probability (Tiered Crypto Verification). A health score quarantines devices that keep failing.
KEYWORDS
OTA updates | Ed25519 | AES-256-CBC | HMAC-SHA256 | replay protection | tiered verification | ESP32
86.7%
of invalid packages rejected before the costly signature gate
75 to 77%
less processing time per invalid package on ESP32, ESP8266 and ATmega328P
720
test packages; every genuine package was accepted
< 2 s
for a device status change to reach the dashboard
Notes: Read the abstract as four ideas: (1) the problem, devices out of sight with unchecked updates; (2) which boards; (3) the three protections: signed firmware, sealed beacons, five ordered gates plus a health score; (4) the results on the right. Say the headline numbers out loud: 86.7 percent of bad packages never reach the expensive signature check, which cuts the time spent on a bad package by about three quarters, and genuine packages are never rejected.

## Slide 3: Problem Definition
Three gaps in how small IoT devices are updated today
Updates and status can be faked
Many update paths skip signature checks, and plain status messages can be forged or replayed. An attacker can install old or altered firmware, or hide a failed device.
The expensive check runs on everything
Ed25519 signature verification is about 75 to 78% of total verification time on the tested boards, yet a cheap check would already reject most invalid images.
No view after deployment
Operators often cannot tell which firmware a node runs or whether an update installed. Manual export, upload and metadata steps cause mismatched releases.
WHY EXISTING WORK FALLS SHORT
Park et al. [5], 2025
Fast and light, but simulated on a laptop; no replay or rollback control
Shin et al. [10], 2024
MQTT, TLS and a Merkle tree; no denial-of-service defence or staged rejection
Carnevale et al. [15], 2023
Firmware freshness on an ESP32 mesh; no timing data and no fleet monitoring
Notes: Problem statement in one line: design an update mechanism for low-cost, mixed microcontrollers that keeps firmware and status traffic authentic and fresh, rejects bad updates cheaply, and shows the operator what every device is running. Then the three gaps. The middle one is our key insight: the most expensive check is usually run first or on everything, although most bad packages could be caught by a 1 ms check. Bottom row: none of the three recent frameworks rejects bad packages in stages, monitors devices or automates signing.

## Slide 4: Objectives
Five goals, each matched to one mechanism in the design
1
Authentic, fresh status
Seal device beacons with AES-256-CBC, an HMAC-SHA256 tag and a persistent counter so forged and replayed beacons are rejected.
2
Automated release signing
Sign every build with Ed25519 inside GitHub Actions, so no manual export, upload or metadata step can produce an unsigned or mismatched release.
3
Cheap early rejection
Order five verification gates by rejection probability per millisecond, so most invalid packages are dropped before the signature check.
4
Safe install and recovery
Check compatibility before release, self-test after boot, roll back on failure and quarantine devices whose health score falls too low.
5
Live fleet visibility
Show each device's verified firmware version and state on a dashboard within 2 seconds of a change.
Notes: Walk down the list: each objective maps to one mechanism we will show in the design slides. 1 sealed beacons, 2 workflow-bound signing, 3 Tiered Crypto Verification, 4 compatibility check, self-test, rollback and quarantine, 5 the live dashboard.

## Slide 5: Hardware and Software Specification
Four microcontroller families, one toolchain per layer
TARGET HARDWARE
ESP32
Dual-core Xtensa LX6, 240 MHz
520 KB SRAM | 4 MB flash
Full pipeline, dual OTA partitions; main demo board
ESP8266
Xtensa L106, 80 MHz
about 80 KB user RAM | up to 4 MB flash
Full five-gate verification
ATmega328P
8-bit AVR, 16 MHz
2 KB SRAM | 32 KB flash
Smallest target in the evaluation
STM32F103
Cortex-M3, 72 MHz
20 KB SRAM | 64 to 128 KB flash
Supported design; measurements planned
SOFTWARE STACK
Firmware | Arduino-ESP32 2.0.17 (C++), PlatformIO or arduino-cli, mbedTLS, ArduinoJson
Gateway | Python 3.11, FastAPI, Uvicorn, cryptography (Ed25519, RSA, AES)
Console | Next.js 16, React 19, TypeScript, Tailwind CSS 4, Clerk sign-in
Data | SQLite (telemetry, audit), JSON gateway state, NeDB, optional Supabase
Flashing | esptool and esptool-js (Web Serial), local USB agent
Release and hosting | GitHub Actions, GitHub Releases, Docker, Cloudflare Tunnel
Host machine | Windows PC, USB data cable (CP210x or CH340 bridge), 2.4 GHz Wi-Fi
Notes: Left: the four board families in the paper. Stress the range, from 520 KB of RAM on the ESP32 down to 2 KB on the ATmega328P. The ESP32 is the demo board; STM32F103 measurements are still planned, so say so. Right: the stack layer by layer, firmware, gateway, console, data, flashing, release and hosting.

## Slide 6: 6.1 Overall Design
Four parts: release pipeline, gateway, devices and operator console
Release pipeline
Version tag starts the build
SHA-256 digest of the image
Signed release bundle
GitHub Releases
OTA gateway (FastAPI)
Releases and signed manifests
Deployments per device
Device registry and tokens
Beacon check: HMAC, counter
Health score and audit log
Device fleet
ESP32 node
ESP8266 node
ATmega328P node
STM32F103 node
publish
manifest + package (HTTPS)
sealed beacons
Operator console (Next.js)
Live fleet view, releases, deployments, USB flashing and provisioning
REST + live stream
USB flash and provisioning (first install)
Notes: Explain left to right. A version tag in the repository starts the build; the workflow hashes and signs the image and publishes a release bundle. The gateway serves the signed manifest and package to devices over HTTPS and receives their sealed beacons. Devices verify every package before installing. The console sits on top of the gateway: it shows the live fleet and is also used once per new board to flash and provision it over USB.

## Slide 7: 6.2 Detailed Design
Complete firmware lifecycle, from tagged build to rollback recovery (paper, Fig. 1)
M1
Tiered Crypto Verification
Five gates check every candidate image, cheapest first
M2
Version-aware policy
Version check and relevance score R before release
M3
Distribution and install
Release delivery and write to the OTA partition
M4
Rollback recovery
Failed post-boot self-test returns to the old image
M5
Health-score quarantine
Low score H stops a device from taking updates
M6
Bundle packaging
Binary, digest, signature, HMAC tag and manifest
Notes: Left is Figure 1 from our paper. Two domains: the developer and GitHub release domain, and the SecureOTA device agent. The device polls, validates the manifest, downloads the signed bundle, runs the five TCV checks, boots the new partition and self-tests it. Pass: commit and raise the health score H. Fail: roll back and lower H. The six mechanisms M1 to M6 on the right are the modules we implemented; the implementation slide explains each.

## Slide 8: 6.3 Database Design
Entities kept by the gateway and the console
DEVICE
gateway state
PK id
arch
fw (running version)
ash (health score)
status, last_seen, ip
authMode, rollbackPending
RELEASE
gateway state
PK id
version
compatible[]
assets: name, size, checksum
imageSha256, securePackage
status, downloadCount
DEPLOYMENT
gateway state
PK id
FK releaseId
version, deviceIds[]
targets: state per device
status, startedAt
success / failure counts
DEVICE_COMMAND
gateway state
PK id
FK deviceId
type (reboot, update...)
status, attempts
requestedBy
createdAt, expiresAt
TELEMETRY
SQLite
FK device_id
ts
ash, rssi
memory, cpu
uptime, fw
AUDIT
SQLite
PK id
ts, actor, source_ip
method, path, status
action, detail
FK device_id
OTA_PROFILES
NeDB / Supabase
PK local_id
clerk_id
username, email
role (admin, operator, viewer)
is_active, last_login_at
OTA_UPLOADS
NeDB / Supabase
PK job_id
FK user_local_id
board_type, com_port
status, progress
started_at, ended_at
1 : N
1 : N
1 : N
Relationships: DEVICE 1 : N TELEMETRY, DEVICE_COMMAND, AUDIT | RELEASE 1 : N DEPLOYMENT | DEPLOYMENT N : M DEVICE (targets) | OTA_PROFILES 1 : N OTA_UPLOADS
Notes: The gateway keeps devices, releases, deployments and per-device commands in its state store, and writes high-volume time series to SQLite: telemetry from every beacon and an audit row for every write request. The console keeps user profiles with roles and USB flash jobs in its own store, mirrored to Supabase when configured. Relationships: a device has many telemetry rows, commands and audit rows; a release has many deployments; a deployment targets many devices.

## Slide 9: 6.4 Algorithm Design
Tiered Crypto Verification (TCV): five gates, the costly signature check last
G1
1.2 ms
Manifest validation
board, version, size
G2
11.8 ms
SHA-256 digest
binary vs manifest
G3
0.9 ms
Image format
header structure
G4
2.3 ms
HMAC verification
package tag
G5
47.5 ms
Ed25519 signature
proves origin
Any gate fails: reject the package, keep the running firmware, lower the health score H
All five pass (D = 1)
write image to the OTA partition
Post-boot self-test
pass: commit, raise H | fail: roll back, lower H
Quarantine
H below threshold: stop polling until an operator acts
KEY EQUATIONS FROM THE PAPER
Install decision
D = g1 × g2 × g3 × g4 × g5 (all gates must pass)
Gate priority
ρi = qi / ci (rejections per ms of cost)
Expected cost of a bad package
E[T] = Σ ci × Π(1 − qj) for j < i
Health score
Hk+1 = min(1, max(0, Hk + α·sk − β·(1 − sk)))
Notes: A package must pass all five gates (D = 1) before it is written to flash. The gates are cheap to expensive: manifest 1.2 ms, digest 11.8 ms, image format 0.9 ms, HMAC 2.3 ms and Ed25519 47.5 ms on the ESP32. The gate priority is rejection probability divided by cost, and the origin-proving Ed25519 gate always goes last. E[T] says a later gate only costs time for packages that survived earlier gates. After install, the post-boot self-test decides commit or rollback, and the health score H moves up by alpha on success and down by beta on failure; below the threshold the device is quarantined.

## Slide 10: 7. Implementation: Modules
Six modules, each built as a part of the working system
M6 Release bundle packaging
CI workflow and build script compile the firmware, compute SHA-256, sign it and package binary, digest, signature and manifest into one release.
M1 Tiered Crypto Verification
Device firmware runs the gate checks in order before writing a single byte to the inactive OTA partition.
M2 Version-aware policy
Gateway offers only the newest compatible release; older versions are refused (anti-rollback). Relevance score R checks capability match.
M3 Distribution and install
Gateway serves signed manifests and packages, tracks deployments per device and confirms them only from the device's reported version.
M4 Rollback recovery
New image boots once in a pending state; a failed self-test returns the board to the previous partition automatically.
M5 Health-score quarantine
Every outcome updates the device health score; a device at or below the threshold stops taking updates until an operator resets it.
Notes: Each module from the design is a real part of the code. Packaging lives in the release workflow and the build script. Verification lives in the device firmware. Policy, distribution and deployment tracking live in the FastAPI gateway. Rollback uses the ESP32 dual-partition boot with a post-boot self-test. The health score is stored on the device and on the gateway, and the console shows it per device. Mention: deployments are marked confirmed only when the device itself reports the new version, not when the gateway has merely sent the file.

## Slide 11: 7. Implementation: The Working Platform
Operator console built on the gateway, used for first install and every update after it
Devices page of the console: fleet summary and the Flash over USB card
1. Build
Build script or CI makes the full image, the signed and encrypted OTA package and build info
2. First flash
Flash over USB from the browser (Web Serial) or the local agent; write Wi-Fi, gateway and device token
3. Publish and deploy
Publish the release; deploy to selected devices; each device updates on its next heartbeat
4. Monitor
Live status, health score, events and audit log for every device
SECURITY BUILT INTO THE PLATFORM
Per-device tokens, revocable from the console
Role-based access: admin, operator, viewer
Every write request recorded in the audit log
Private keys never stored in the repository
Notes: This is the real console. Walk the four steps on the right in the order you would demo them: build, first flash over USB, publish and deploy, monitor. If there is time for a live demo, show the Devices page, then the Releases page, then a deployment completing. Bottom box: the platform-level protections around the cryptography.

## Slide 12: 8. Results and Discussion: Gate Statistics
360 invalid test packages through the five gates on the ESP32 (paper, Table I)
Chart: Invalid packages reaching and rejected at each gate
| G1 Manifest | G2 SHA-256 | G3 Format | G4 HMAC | G5 Ed25519
Reaching the gate | 360 | 240 | 120 | 60 | 48
Rejected at the gate | 120 | 120 | 60 | 12 | 48
312 of 360
invalid packages (86.7%) were rejected by the first four gates, so they never needed the 47.5 ms signature check.
READING THE CHART
Manifest check catches wrong board and outdated versions at 1.2 ms.
Digest and format checks catch altered, corrupted and malformed images.
Only forged signatures reach G5; all 48 were rejected there.
All genuine packages were accepted, so nothing valid was lost.
Notes: Each pair of bars is one gate: how many invalid packages reached it, and how many it rejected. The manifest gate removes a third at 1.2 ms. Digest and format checks remove most of the rest. Only 48 forged-signature packages ever reach the Ed25519 gate, which costs about 75 percent of the whole pipeline. So 312 of 360, 86.7 percent, are rejected before the expensive gate, and no genuine package was rejected.

## Slide 13: 8. Results and Discussion: Verification Time
Full pipeline time vs expected TCV time per invalid package (paper, Table II and Fig. 4)
Chart: Verification time per invalid package (ms)
| ESP32 | ESP8266 | ATmega328P
Full pipeline (ms) | 63.7 | 119.2 | 429
TCV expected time (ms) | 16.1 | 27.9 | 106.1
Platform | Full (ms) | TCV (ms) | Saved | Ed25519 share
ESP32 | 63.7 | 16.1 | 74.8% | 74.6%
ESP8266 | 119.2 | 27.9 | 76.6% | 78.2%
ATmega328P | 429.0 | 106.1 | 75.3% | 75.9%
DISCUSSION
Savings stay between 75 and 77% on all three boards, although their speeds differ by 7 times.
The reason: Ed25519 is a similar share of the pipeline everywhere (75 to 78%), and most bad packages never reach it.
Framework cost on flash: 11 KB to 30 KB.
Notes: Grey bars are the time a package would take if every gate always ran; green bars are the expected time under our ordering for an invalid package. On the ESP32 that is 63.7 ms down to 16.1 ms; on the ATmega328P 429 ms down to 106.1 ms. The saving is almost the same everywhere, about three quarters, because the signature check is about three quarters of the pipeline on every board and most bad packages never reach it.

## Slide 14: 8. Results and Discussion: Comparison
SecureOTA against three recent secure OTA frameworks (paper, Table III)
 | Carnevale et al. [15] | Shin et al. [10] | Park et al. [5] | SecureOTA (ours)
Evaluation platform | ESP32 wireless mesh | MQTT OTA for software-defined vehicles | Python on an Intel i7 laptop | ESP32, ESP8266, ATmega328P
Firmware protection | Key pairing and digital signature | TLS plus Merkle tree root hash | Dual XOR with key table, DEFLATE | SHA-256, HMAC and Ed25519 signature
Replay / rollback control | Freshness quarantine | Merkle tree detects duplicate updates | Not addressed | Persistent counter and version-aware policy
Staged early rejection | No | No | No | Yes, five-gate TCV (86.7% before signature)
Authenticated device status | Not stated | No | No | Yes, sealed beacons, dashboard under 2 s
Automated signing and release | No | No | No | Yes, GitHub Actions with Ed25519
None of the three rejects bad packages in stages, monitors devices or automates signing. SecureOTA does all three on real boards, with measured timings.
Notes: Read across the green column. Park et al. is fast but was simulated on a laptop and does not handle replay or rollback. Shin et al. show MQTT over TLS is about four times faster than HTTPS and detect duplicate updates, but have no staged rejection and no defence against denial of service. Carnevale et al. keep firmware fresh on an ESP32 mesh but report no timing. Be fair: these works target different settings; our claim is the combination of staged rejection, authenticated monitoring and automated signing on real microcontrollers.

## Slide 15: 9. Conclusion
What SecureOTA achieves
Trusted updates and status
Workflow-bound Ed25519 signing and sealed beacons with HMAC and persistent counters stop forged and replayed firmware and status.
Cheap rejection of bad packages
86.7% of invalid packages are dropped before the signature gate; the time spent on a bad package falls by about 75% on all three boards.
Self-healing fleet
Post-boot self-test, automatic rollback and health-score quarantine remove failing devices from the update cycle without an operator.
SecureOTA gives low-cost, mixed IoT hardware verified updates and an authenticated live view of the fleet, at a flash cost of 11 KB to 30 KB.
Notes: Summarise in three sentences, one per card, then read the bottom line. Keep it short; the numbers have already been shown.

## Slide 16: 10. Future Enhancements
Next steps named in the paper
01
STM32F103 measurements
Complete the timing and memory evaluation on the Cortex-M3 board.
02
Key provisioning and rotation
Secure first-time key provisioning and scheduled rotation of device keys.
03
Energy per update
Measure the energy each update costs on battery-powered nodes.
04
Larger fleets, noisy links
Evaluate bigger fleets over lossy, congested wireless networks.
05
Adaptive gate ordering
Re-order the gates online as the observed rejection rates change.
06
Post-quantum signatures
Support post-quantum signature schemes alongside Ed25519.
Notes: Six directions from the paper's conclusion. The first is the honest gap: STM32F103 measurements are not done yet. The last is the long-term one: post-quantum signatures, since Ed25519 is not quantum-safe.

## Slide 17: 11. Patent / Paper Publications
Research output from this project
CONFERENCE PAPER
SecureOTA: A Secure Heterogeneous OTA Update Mechanism for Resource-Constrained IoT Devices
Priyankaa Devi S, Rithik Sharma A, Ritesh V, and the project guide
Department of Cybersecurity Engineering, KCG College of Technology, Chennai
Status
Prepared for submission
Target venue
[IEEE conference name, year]
Format
IEEE conference paper, 16 references
PATENT
[Patent status to be confirmed]
Candidate novel elements: the cost-ordered five-gate verification pipeline (TCV) and the health-score quarantine loop. Prior disclosure in the paper should be checked with the institution before filing.
Notes: State the paper status exactly as it is on the day: prepared for submission, with the target conference. If the venue or patent status is confirmed before the exam, replace the placeholders. Do not claim acceptance or a filed patent unless that has happened.

## Slide 18: 12. References
As cited in the paper
[1] Noprianto, N. Funabiki, H. H. S. Kyaw, K. C. Brata, I. N. D. Kotama, "A proposal of secure and automated over-the-air firmware update mechanism for IoT devices using CI/CD," Sensors, vol. 26, no. 5, 1535, 2026.
[2] H. S. Mehdy, M. E. Rusli, H. K. Hoomod, "A secured parallel multi-broker MQTT framework with chaos-enhanced hybrid encryption for repetition-resistant IoT security," Computers, vol. 15, no. 10, 650, 2026.
[3] G. Amirkhanova et al., "A lightweight, end-to-end encrypted data pipeline for IIoT: An AES-GCM implementation for ESP32, MQTT, and Raspberry Pi," Information, vol. 17, no. 1, 33, 2026.
[4] W. Y. Leong, "Quantum-resistant encryption for IoT communication in critical engineering infrastructure," Eng. Proc., vol. 134, no. 1, 76, 2026.
[5] C.-Y. Park, S.-J. Lee, I.-G. Lee, "Secure and lightweight firmware over-the-air update mechanism for Internet of Things," Electronics, vol. 14, no. 8, 1583, 2025.
[6] L. Formanek, M. Kubaščík, O. Karpíš, P. Kolok, "Advanced system for remote updates on ESP32-based devices using over-the-air update technology," Computers, vol. 14, no. 12, 531, 2025.
[7] F. Serepas et al., "Lightweight embedded IoT gateway for smart homes based on an ESP32 microcontroller," Computers, vol. 14, no. 9, 391, 2025.
[8] C.-G. Dumitrache, P. Anghelescu, "Design and implementation of a secure communication architecture for IoT devices," J. Sens. Actuator Netw., vol. 14, no. 4, 64, 2025.
[9] V. P. Ojha, S. Chauhan, S. Yarahmadian, D. Carvalho, "Unfolding post-quantum cryptosystems: CRYSTALS-Dilithium, McEliece, BIKE, and HQC," Mathematics, vol. 13, no. 17, 2841, 2025.
[10] Y. Shin, S. Jeon, "MQTree: Secure OTA protocol using MQTT and MerkleTree," Sensors, vol. 24, no. 5, 1447, 2024.
[11] V. Bhargava, N. S. Raghava, "Version control system gateway to optimize firmware over the air (FOTA) update for IoT wireless devices," Wireless Pers. Commun., vol. 134, no. 1, pp. 249-265, 2024.
[12] C. Silva, V. A. Cunha, J. P. Barraca, R. L. Aguiar, "Analysis of the cryptographic algorithms in IoT communications," Inf. Syst. Front., vol. 26, pp. 1243-1260, 2024.
[13] I. Radhakrishnan, S. Jadon, P. B. Honnavalli, "Efficiency and security evaluation of lightweight cryptographic algorithms for resource-constrained IoT devices," Sensors, vol. 24, no. 12, 4008, 2024.
[14] F. C. Andriulo, M. N. Postorino, "Edge computing and cloud computing for Internet of Things: A review," Informatics, vol. 11, no. 4, 71, 2024.
[15] L. Carnevale et al., "Secure and energy efficient filtered over-the-air Internet of Things setup in a wireless mesh network for firmware freshness," Proc. IEEE BigData, Sorrento, Italy, pp. 3904-3913, 2023.
[16] Z. Dewamuni, B. Shanmugam, S. Azam, S. Thennadil, "Bibliometric analysis of IoT lightweight cryptography," Information, vol. 14, no. 12, 635, 2023.
Notes: No need to read these out. If asked, the three most relevant comparisons are [5] Park, [10] Shin and [15] Carnevale.